January 2016

| Americas Bosch Security Systems, Inc. 130 Perinton Parkway Fairport, New York, 14450, USA Phone: + 1 800 289 0096 Fax: +1 585 223 9180 security.sales@us.bosch.com www.boschsecurity.us | Europe, Middle East, Africa Bosch Security Systems B.V. P.O. Box 80002 5600 JB Eindhoven, The Netherlands Phone: + 31 40 2577 284 Fax: +31 40 2577 330 emea.securitysystems@bosch.com www.boschsecurity.com | Asia-Pacific Bosch Security Systems Pte Ltd 38C Jalan Pemimpin Singapore 577180 Phone: +65 6319 3450 Fax: +65 6319 3499 apr.securitysystems@bosch.com www.boschsecurity.com |
| --- | --- | --- |

Product Guide Specification

SECTION 28 23 19

DIGITAL VIDEO RECORDERS AND ANALOG RECORDING DEVICES

BOSCH DIVAR IP 5000 DIGITAL VIDEO RECORDER

- – GENERAL

  - SUMMARY

    - Section Includes

      - Section 28 23 23 – Video Surveillance Systems Infrastructure

    - Related Sections

      - Section [28 23 13 – Video Surveillance Control and Management Systems]

      - Section [28 23 16 – Video Surveillance Monitoring and Supervisory Interfaces]

      - Section [28 23 23 – Video Surveillance Systems Infrastructure]

      - Section [28 23 29 – Video Surveillance Remote Devices]

**********Specifier’s note: Include those standards referenced elsewhere in this SECTION.

  - REFERENCES

    - Australia and New Zealand Standards

      - AS/NZS CISPR 22

    - Canadian Standards Association (CSA)

      - CSA 60950

      - ICES-003

    - Emissions/Immunity

      - MIC

      - VCCI

      - CoC (South Africa)

      - BSMI

      - KN22

      - KN24

      - CISPR 24

    - European Norm (CE)

      - Complies with CE requirements

      - EN 60950

      - EN60825-1

      - EN55022

      - EN55024

      - EN61000-4-2

      - EN61000-4-3

      - EN61000-4-4

      - EN61000-4-5

      - EN61000-4-6

      - EN61000-4-11

    - Federal Communications Commission (FCC) (www.fcc.gov)

      - FCC Part 15 Class A

    - International Electrotechnical Commission (IEC)

      - IEC61000-3-2

      - IEC61000-3-3

    - International Organization for Standardization (ISO)

      - 9001 – Quality System

    - Safety

      - CB IEC60950-1 (all national deviations)

      - GOST-R

      - BSMI CNS14336

      - CCC GB 4943-2001

      - SABS, S Resolution 92-98

    - Underwriters Laboratories, Inc. (UL) (www.ul.com)

      - UL 60950

  - DEFINITIONS

    - Solid-state drive (SSD): Solid-state, non-volatile storage-device that contains a   backup image of all system software needed to a full system recovery.

    - RAID: Redundant Array of Independent Disks is a technology that employs the simultaneous use of two or more hard disk drives to achieve greater levels of performance, reliability, and/or larger data volume sizes.

    - iSCSI: Internet SCSI is a protocol that allows clients (called initiators) to send SCSI commands to SCSI storage devices (targets) on remote servers via an IP network.

    - SNMP: Simple Network Management Protocol is a component of the Internet Protocol Suite as defined by the Internet Engineering Task Force (IETF). SNMP is used in network management systems to monitor network-attached devices for conditions that warrant administrative attention.

  - SYSTEM DESCRIPTION

    - Digital Video Recorders.

      - Digital Video Recorder and Storage

    - Performance Requirements

      - The digital video recorder shall be an all-in-one recording solution for network surveillance systems of up to 32 channels and 310 Mbps incoming bandwidth.

      - The digital video recorder shall be a pre-configured and pre-installed IP video recording solution with up to 16 TB (4 x 4 TB) storage capacity.

      - The digital video recorder shall offer front-swappable SATA-II hard drives providing 16 TB of gross storage capacity.

      - The digital video recorder shall run the Video Streaming Gateway to allow third-party camera integration.

      - The digital video recorder shall allow remote viewing via the Bosch Video Security App and the Bosch Video Security Client.

      - The digital video recorder shall offer Web Client software.

      - The digital video recorder shall support mobile devices (iOS and Android).

      - The digital video recorder shall offer 12MP real time recording.

      - The digital video recorder shall offer 12 MP IP camera support for view and playback.

      - Bosch offers its customers free cloud based remote access (connectivity service) for easy remote access to network-connected devices.

      - The digital video recorder shall provide tamper protection.

      - The digital video recorder shall provide remote alarm notification.

      - The digital video recorder shall offer up to 12 MP IP camera support for remote viewing and playback.

  - SUBMITTALS

    - Submit under provisions of Section [01 33 00.]

    - Product Data:

      - Manufacturer’s data, operator and installation manuals software programs.

    - Shop Drawings; include

      - System device locations on architectural floor plans.

      - Full Schematic of system, including wiring information for all devices.

    - Closeout Submittals

      - User manuals (including Parts list and Connection diagram).

  - QUALITY ASSURANCE

    - Manufacturer:

      - Minimum of [10] years experience in manufacture and design Video Surveillance Devices.

    - Manufacturer’s quality system: Registered to ISO 9001:2000 Quality Standard.

    - Installer:

      - Minimum of [5] years experience installing Video Surveillance System.

  - DELIVERY, STORAGE AND HANDLING

    - Comply with requirements of Section 01 60 00.

    - Deliver materials in manufacture’s original, unopened, undamaged containers; and unharmed original identification labels.

    - Protect store materials from environmental and temperature conditions following manufacturer’s instructions.

    - Handle and operate products and systems according to manufacturer’s instructions.

    - Bosch provides off-the-shelf availability for our top selling products and same-day or 24-hour shipping.

  - WARRANTY

    - Provide manufacturer’s warranty covering [3] years for CCTV products to repair and replace defective equipment.

    - Exchanges available for product failures.

  - MAINTENANCE

    - Make ordering of new equipment for expansions, replacements, and spare parts available to dealers and end users.

    - Provide factory direct technical support from 8:00 a.m. to 8:00 p.m. via phone or e-mail, or any time via Web.

      - Provide toll-free numbers to contact customer support.

    - Provide on-site training and on-line training via web.

- – PRODUCTS

  - MANUFACTURERS

    - Acceptable Manufacturer:

[Bosch Security Systems, Inc.

130 Perinton Parkway

Fairport, New York, 1450, USA

Phone: + 1 800 289 0096

Fax: + 1 585 223 9180

security.sales@us.bosch.com

www.boschsecurity.us]

[Bosch Security Systems B.V.

P.O. Box 80002

5600 JB Eindhoven, The Netherlands

Phone: + 31 40 2577 284

Fax: +31 40 2577 330

emea.securitysystems@bosch.com

www.boschsecurity.com]

Robert Bosch (SEA) Pte Ltd

11 Bishan Street 21

Singapore 573943

Phone: +65 6258 5511

Fax: +65 6571 2699

apr.securitysystems@bosch.com

www.boschsecurity.com

    - Substitutions: [Not permitted.] [Under provisions of Division 1.]

      - [All proposed substitutions must be approved by the Architect or Engineer professional.]

      - [Proposed substitutions must provide a line-by-line compliance documentation.]

  - BOSCH DIVAR IP 5000 [DIP-5042EZ-0HD][DIP-5042EZ-1HD][DIP-5042EZ-2HD][DIP-5042EZ-4HD][DIP-5044EZ-1HD][DIP-5044EZ-2HD][DIP-5044EZ-4HD][DIP-5042EZ-0HDX][DIP-5042EZ-1HDX][DIP-5042EZ-2HDX][DIP-5042EZ-4HDX][DIP-5044EZ-1HDX][DIP-5044EZ-2HDX][DIP-5044EZ-4HDX]

    - General Characteristics:

      - The digital video recorder shall be an all-in-one recording solution for network surveillance systems of up to 32 channels.

      - The digital video recorder shall be a pre-configured and pre-installed IP video recording solution with up to 16 TB (4 x 4 TB) storage capacity.

      - The digital video recorder shall offer front-swappable SATA-II hard drives providing 16 TB of gross storage capacity.

      - The digital video recorder shall run the Video Streaming Gateway to allow third-party camera integration.

      - The digital video recorder shall allow remote viewing via the Bosch Video Security App and the Bosch Video Security Client.

      - The digital video recorder shall offer a maximum of 16 TB of gross capacity storage with a corresponding 14896 GB of net storage capacity.

      - The digital video recorder shall offer a bandwidth of 310 Mbit/s (read and write) with Bosch IP-cameras/encoders and equipped with 4 HDDs.

      - The digital video recorder shall offer an Intel Atom N3150 processer + Marvell 88SE9215 storage controller.

      - The digital video recorder shall utilize Microsoft Windows Storage Server 2012 R2 (64-bit).

      - The digital video recorder shall have tamper-protection.

      - The digital video recorder shall offer comprehensive search and playback functions.

      - The digital video recorder shall offer remote search and playback functions.

      - The digital video recorder shall allow viewing, playback and configuration via a remote Web management connection.

      - The digital video recorder shall operate a Windows based operating system.

    - Functions

      - The digital video recorder shall come pre-installed and pre-configured with all necessary software.

      - The digital video recorder shall enable viewing of high-quality UHD video despite low or limited bandwidth by utilizing Dynamic Transcoding technology.

      - The digital video recorder shall decode and decompress the data stream to a lower bit rate stream tailored to the bandwidth of the connection.

      - The digital video recorder shall offer SSD; a solid-state, non-volatile memory module that contains a backup image of all system software needed to a full system recovery.

      - The digital video recorder shall have Alarm-Inputs (2) and Relay-Outputs (2).

    - Recording

      - The digital video recorder shall simultaneously record a maximum 32 channels

      - The digital video recorder shall record at up to 310 Mbps per channel.

      - The digital video recorder shall allow manual and automatic recording.

      - The digital video recorder shall allow automatic recording via a schedule or based on an alarm.

    - Management

      - The digital video recorder shall provide a browser-based user interface for system configuration and unified appliance management.

      - Alternatively, the digital video recorder shall allow operators to use one central tool for configuration and operations management.

    - Control

      - The digital video recorder shall provide alarm inputs/outputs on the rear panel of the device.

      - The digital video recorder shall support the use of PC software or a built-in web application via a network for live viewing, playback and configuration.

      - The digital video recorder shall contain a 10/100/1000Base-T Ethernet ports for local or wide area network connection.

    - Remote Viewing

      - The digital video recorder shall provide the Bosch Video Security Client for remote viewing.

      - Bosch offers its customers a connectivity service (DDNS) for access to network-connected devices without any advanced network configuration.

    - Processor

      - The digital video recorder shall contain an Intel Intel Atom N3150 + Marvell 88SE9215 storage controller.

      - The digital video recorder processor shall contain one (1) socket.

    - Memory

      - The digital video recorder shall have a DDR3L SO-DIMM memory type.

      - The IP Video Storage System shall offer a 1333 MHz maximum front side bus.

      - The IP Video Storage System shall come with 4 GB, DDR3-1333 SO-DIMM (1 x 4 GB), of memory installed.

    - Storage

      - The digital video recorder shall contain four (4) 3.5 in. SATA storage trays.

      - The digital video recorder shall have four a maximum of (4) HDD hard drives installed.

      - The digital video recorder shall include a graphics memory controller integrated in the Intel Atom N3150 processor.

      - The digital video recorder shall include a 2x1 GbE Rj45 network port.

    - Electrical:

      - Power Supply: 220 W (100/240 VAC)

      - Energy Efficiency: Energy Star compliant power supply

    - Mechanical

      - Form Factor: 4-bay mini tower

      - Power Supply: 1 x internal power supply

      - USB Ports: 4 x USB 3.0 ports

      - Network: 2 x Gigabit Ethernet LAN

      - Dimensions (H x W x D): 180 x 200 x 212 mm (7.09 x 7.87 x 8.35 in.)

      - Weight:

        - Without HDD: 4.25 kg (9.37 lb)

        - Fully loaded: 6.75 kg (14.88)

    - Environmental:

      - Operating Temperature: +10°C to +35°C (+50°F to +95°F)

      - Non-operating Temperature: –40°C to +70°C (–40°F to +158°F)

      - Operating Relative Humidity: 8 to 90%, non-condensing

      - Non-operating Relative Humidity: 5 to 95%, non-condensing

    - Accessories:

      - DVR-XS200-A: Storage Expansion Kit 2TB HDD

      - DVR-XS400-A: Storage Expansion Kit 4TB HDD

- – EXECUTION

  - EXAMINATION

    - Examine areas to receive devices and notify adverse conditions affecting installation or subsequent operation.

    - Do not begin installation until unacceptable conditions are corrected.

  - PREPARATION

    - Protect devices from damage during construction.

  - INSTALLATION

    - Install devices in accordance with manufacturer’s instruction at locations indicated on the floor drawings plans.

    - Perform installation with qualified service personnel.

    - Install devices in accordance with the National Electrical Code or applicable local codes.

    - Ensure selected location is secure and offers protection from accidental damage.

    - Location must provide reasonable temperature and humidity conditions, free from sources of electrical and electromagnetic interference.

  - FIELD QUALITY CONTROL

    - Test snugness of mounting screws of all installed equipment.

    - Test proper operation of all video system devices.

    - Determine and report all problems to the manufacturer’s customer service department.

  - ADJUSTING

    - Make proper adjustment to video system devices for correct operation in accordance with manufacturer’s instructions.

    - Make any adjustment of camera settings to comply with specific customer’s need.

  - DEMONSTRATION

    - Demonstrate at final inspection that video management system and devices functions properly.

END OF SECTION

# Text boxes

Specifier Notes:  This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format, based on MasterFormat 2004 and The Project Resource Manual—CSI Manual of Practice. The Manufacturer is responsible for technical accuracy.

The section must be carefully reviewed and edited by the Architect or Engineer to meet the requirements of the project and local building code.  Words and sentences within brackets [ ] are choices to include or exclude a particular item or statement.  Coordinate this section with other specification sections and the Drawings.  Delete all “Specifier Notes” after editing this section.