April 2013

| Americas Bosch Security Systems, Inc. 130 Perinton Parkway Fairport, New York, 14450, USA Phone: + 1 800 289 0096 Fax: +1 585 223 9180 security.sales@us.bosch.com www.boschsecurity.us | Europe, Middle East, Africa Bosch Security Systems B.V. P.O. Box 80002 5600 JB Eindhoven, The Netherlands Phone: + 31 40 2577 284 Fax: +31 40 2577 330 emea.securitysystems@bosch.com www.boschsecurity.com | Asia-Pacific Robert Bosch (SEA) Pte Ltd, Security Systems 11 Bishan Street 21 Singapore 573943 Phone: +65 6571 2600 Fax: +65 6571 2698 apr.securitysystems@bosch.com www.boschsecurity.com |
| --- | --- | --- |

Product Guide Specification

SECTION 28 23 29

VIDEO SURVEILLANCE REMOTE DEVICES AND SENSORS

BOSCH AUTODOME 4000 MINI PTZ DOME

- – GENERAL

  - SUMMARY

    - Section Includes

      - Security Lighting

    - Related Sections

      - Section [28 23 13 – Video Surveillance Control and Management Systems].

      - Section [28 23 16 – Video Surveillance Monitoring and Supervisory Interfaces].

      - Section [28 23 19 – Digital Video Recorders and Analog Recording Devices].

      - Section [28 23 23 – Video Surveillance Systems Infrastructure].

**********Specifier’s note: Include those standards referenced elsewhere in this SECTION.

  - REFERENCES

    - Australia Standards

      - Complies with CTICK standards.

    - European Norm

      - Complies with CE Electromagnetic Compatibility regulations

      - Complies with CE Product Safety regulations

    - Federal Communications Commission (FCC) (www.fcc.gov)

      - Complies with FCC Part 15.

    - Underwriters Laboratories, Inc. (UL) (www.ul.com)

      - Complies with UL standards.

  - SYSTEM DESCRIPTION

    - Section Includes

      - Video Surveillance Remote Devices

    - Performance Requirements

      - The mini PTZ dome shall offer 26x optical zoom with a resolution of 600 TVL.

      - The mini PTZ dome shall be a true day/night camera.

      - The mini PTZ dome shall offer Wide Dynamic Range (WDR).

      - The mini PTZ dome camera shall be enclosed in a compact and vandal-resistant (IK10 rated) enclosure.

      - The mini PTZ dome shall be IP66 rated making it suitable for indoor and outdoor use.

      - The mini PTZ dome shall be equipped with an internal heater making the dome suitable for use in ambient temperature of –40° to +50°C (–40°F to +122°F).

  - SUBMITTALS

    - Submit under provisions of Section [01 33 00.]

    - Product Data:

      - Manufacturer’s data, user and installation manuals for all equipment and software programs including computer equipment and other equipment required for complete video management system.

    - Shop Drawings; include

      - System device locations on architectural floor plans.

      - Full Schematic of system, including wiring information for all devices.

    - Closeout Submittals

      - User manual.

      - Parts list.

      - System device locations on architectural floor plans.

      - Wiring and connection diagram.

      - Maintenance requirements.

  - QUALITY ASSURANCE

    - Manufacturer:

      - Minimum of [10] years experience in manufacture and design Video Surveillance Devices.

    - Video Surveillance System:

      - Listed by CSA.

      - Certified compliant to FCC and CE for the required loads.  Test methods are in accordance with Industry Canada and the IEC.  Provide evidence of compliance upon request.

    - Installer:

      - Minimum of [5] years experience installing Video Surveillance System.

  - DELIVERY, STORAGE AND HANDLING

    - Comply with requirements of Section 01 60 00.

    - Deliver materials in manufacture’s original, unopened, undamaged containers; and unharmed original identification labels.

    - Protect store materials from environmental and temperature conditions following manufacturer’s instructions.

    - Handle and operate products and systems according to manufacturer’s instructions.

    - Bosch provides off-the-shelf availability for our top selling products and same-day or 24-hour shipping.

  - WARRANTY

    - Provide manufacturer’s warranty covering 3 years for replacement and repair of defective equipment.

  - MAINTENANCE

    - Make ordering of new equipment for expansions, replacements, and spare parts available to dealers and end users.

    - Provide factory direct technical support from 8:00 a.m. to 8:00 p.m. via phone and e-mail.

- – PRODUCTS

  - MANUFACTURERS

    - Acceptable Manufacturer:

[Bosch Security Systems, Inc.

130 Perinton Parkway

Fairport, New York, 1450, USA

Phone: + 1 800 289 0096

Fax: + 1 585 223 9180

security.sales@us.bosch.com

www.boschsecurity.us]

[Bosch Security Systems B.V.

P.O. Box 80002

5600 JB Eindhoven, The Netherlands

Phone: + 31 40 2577 284

Fax: +31 40 2577 330

emea.securitysystems@bosch.com

www.boschsecurity.com]

[Asia-Pacific

Robert Bosch (SEA) Pte Ltd, Security Systems

11 Bishan Street 21

Singapore 573943

Phone: +65 6571 2600

Fax: +65 6571 2698

apr.securitysystems@bosch.com

www.boschsecurity.com]

    - Substitutions: [Not permitted.] [Under provisions of Division 1.]

      - [All proposed substitutions must be approved by the Architect or Engineer professional.]

      - [Proposed substitutions must provide a line-by-line compliance documentation.]

  - BOSCH AUTODOME 4000 MINI PTZ DOME [VEZ-413-EWCS] [VEZ-413-ECCS VEZ] 
[VEZ-413-EWTS] [VEZ-413-ECTS] [VEZ-423-EWCS] [VEZ-423-ECCS VEZ] 
[VEZ-423-EWTS] [VEZ-423-ECTS]

    - Imaging:

      - The mini PTZ dome shall come with a ¼" Double Scan Super HAD CCD II imager.

      - The mini PTZ dome shall offer the following pixel elements:

        - PAL: 976 (H) x 582 (V)

        - NTSC: 976 (H) x 494 (V)

      - The mini PTZ dome shall offer a horizontal resolution of 600 TVL (NTSC and PAL).

      - The mini PTZ dome shall offer 26X effective optical zoom.

      - The mini PTZ dome shall offer 10X digital zoom.

      - The mini PTZ dome shall offer the following minimum illumination:

        - 0.2 Lux/ F1.65

        - 0.001 Lux/DSS

        - 0.1 Lux/ICR

      - The mini PTZ dome shall be a true day/night camera.

      - The mini PTZ dome shall possess Dynamic Noise Reduction (DNR).

      - The mini PTZ dome shall offer Wide Dynamic Range (WDR).

    - Communications:

      - The mini PTZ dome shall utilize RS-485 and Bosch Biphase (with converter, sold separately) for camera setup and control.

      - The mini PTZ dome shall support the Bosch (OSRD) and the Pelco P/D communication protocols (also Bosch Biphase protocol, with a second converter, sold separately).

    - Operation

      - The mini PTZ dome shall have a pan range of 360°, continuous.

      - The mini PTZ dome shall have a tilt range of between 0° to 180°.

      - The mini PTZ dome shall offer eight (8) auto scan modes, including a vector scan.

      - The mini PTZ dome shall have a preposition speed of 360° per second.

      - The mini PTZ dome shall offer 210 preset positions.

      - The mini PTZ dome shall offer eight (8) tours and eight (8) patterns.

      - The mini PTZ dome shall offer four (4) alarm inputs (normal dry contacts) and one (1) alarm output (normal relay 5 VDC/40 mA maximum).

      - The mini PTZ dome shall offer the following language support for the on-display menus: English, Chinese, Dutch, French, German, Italian, Russian and Spanish.

    - Electrical

      - The mini PTZ dome shall require 24 VAC ± 10%, 50/60 Hz.

      - The mini PTZ dome shall come with built-in power line surge.

      - The mini PTZ dome shall consume the following power:

        - without heater: 24 VAC, 850 mA / 20 W

        - with heater: 24 VAC, 2 A / 45 W

    - Environmental

      - The mini PTZ dome shall have an ingress rating of IP66.

      - The mini PTZ dome shall have an impact rating of IK10.

      - The mini PTZ dome shall operate in the following temperature ranges:

        - without heater: –10°C to +50°C (14°F to +122°F)

        - with heater: –40°C to +50°C (–40°F to +122°F)

    - Construction

      - The mini PTZ dome housing shall be constructed of cast aluminum.

      - The mini PTZ dome bubble shall be constructed of polycarbonate.

      - The mini PTZ dome housing shall be offered in white or charcoal.

    - Camera:

      - Imager: ¼" Double Scan Super HAD CCD II

      - Lens Size: fW=3.49 ±0.17 mm fT=104.02 ±5.20 mm 
(30X +/- 10% Optical Zoom)

      - Effective Pixels:

        - PAL: 976 (H) x 582 (V)

        - NTSC: 976 (H) x 494 (V)

      - Horizontal Resolution: 600 TVL (NTSC, PAL)

      - Optical Zoom: 26x, effective

      - Digital Zoom: 10x

      - Field of View: 2.46° (TELE) to 69.5° (Wide)

      - Focus: Automatic with manual override

      - Signal-to-Noise Ratio (SNR): >50 dB

      - White Balance: Auto, indoor, outdoor, one push

      - Minimum Illumination:

        - 0.2 Lux/ F1.65

        - 0.001 Lux/DSS

        - 0.1 Lux/ICR

      - Iris Control: Auto

      - Wide Dynamic Range: On/Off

      - Dynamic Noise Reduction: 3DNR

      - Privacy: 15 zones, maximum

    - Mechanical

      - Weight: 1.5 kg (3.3 lb)

      - Pan Range: 360° continuous

      - Tilt Range: 0° to 180° (90° when 3D Privacy Masking is enabled)

      - Flip: Rotate 180° at bottom of tilt

      - Auto Scan: 8 Auto Scan modes including vector scan

      - Pre-position Speed: 360°/s

      - Preset Positions: 210 Positions with camera status

      - Tours: 8 Tours (Preset, Pattern, Scan)

      - Patterns: 8 Patterns

      - On-Screen Display (OSD): Camera ID, Title, Mode, and Angle (Multi-Language)

      - Multi-language OSD: English, Chinese, Dutch, French, German, Italian, Russian, Spanish

    - Electrical

      - Power Supply: 24 VAC ± 10%, 50/60 Hz, Built-in power line surge

      - Power Requirements: 24 VAC adapter, 1 A (2.5 A with heater)

      - Power Consumption: 24 VAC, 850 mA / 20 W (without heater), 
24 VAC, 2 A / 45 W (with heater)

      - Alarm Input: 4 normal dry contacts (selectable NC/NO)

      - Alarm Output: 1 normal relay 5 VDC/40 mA maximum (selectable NC/NO)

      - Control: RS-485; baud rate: 2400-38.4 Kbps (default = 9600 bps)

      - Access Time: 0.75 second maximum preset recall time

      - Camera Address (ID): Physical - 99

    - Environmental:

      - Ingress Rating: IP66

      - Impact Rating: IK10

      - Operating Temperature:

        - without heater: –10°C to 50°C (14°F to 122°F)

        - with heater: –40°C to 50°C (–40°F to 122°F)

      - Heater Thermostat: On/Off at 0°C to 10°C (32°F to 50°F)

      - Installation Humidity: 80% relative humidity (RH)

      - Storage Temperature: –20°C to 60°C (–4°F to 140°F)

    - Communications

      - Camera Setup/Control: RS-485; also Bosch Biphase with converter (sold separately)

      - Communications Protocol: Bosch (OSRD), Pelco P/D (Also Bosch Biphase protocol, with a second converter, sold separately.)

    - Construction:

      - Housing Material: Cast aluminum

      - Color: White or charcoal

      - Size (Diameter x Height): ø154 x 138 mm (H)

      - Bubble: ø112 mm Polycarbonate, clear or tinted

- – EXECUTION

  - EXAMINATION

    - Examine areas to receive devices and notify adverse conditions affecting installation or subsequent operation.

    - Do not begin installation until unacceptable conditions are corrected.

  - PREPARATION

    - Protect devices from damage during construction.

  - INSTALLATION

    - Install devices in accordance with manufacturer’s instruction at locations indicated on the floor drawings plans.

    - Perform installation with qualified service personnel.

    - Install devices in accordance with the National Electrical Code or applicable local codes.

    - Ensure selected location is secure and offers protection from accidental damage.

    - Location must provide reasonable temperature and humidity conditions, free from sources of electrical and electromagnetic interference.

  - FIELD QUALITY CONTROL

    - Test snugness of mounting screws of all installed equipment.

    - Test proper operation of all video system devices.

    - Determine and report all problems to the manufacturer’s customer service department.

  - ADJUSTING

    - Make proper adjustment to video system devices for correct operation in accordance with manufacturer’s instructions.

    - Make any adjustment of camera settings to comply with specific customer’s need.

  - DEMOSTRATION

    - Demonstrate at final inspection that video management system and devices functions properly.

END OF SECTION

# Text boxes

Specifier Notes:  This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format, based on MasterFormat 2004 and The Project Resource Manual—CSI Manual of Practice. The Manufacturer is responsible for technical accuracy.

The section must be carefully reviewed and edited by the Architect or Engineer to meet the requirements of the project and local building code.  Words and sentences within brackets [ ] are choices to include or exclude a particular item or statement.  Coordinate this section with other specification sections and the Drawings.  Delete all “Specifier Notes” after editing this section.