### PLENA call station LBB1941/00

### Architects’ and Engineers’ Specifications

The call station shall have a metal base for stability, a flexible microphone stem and a uni-directional condenser microphone.

It shall be part of a sound amplification system, such that there is a direct connection between the call station and a matching amplifier, or between the call station and another call station in the same system. The call station shall have a 5m interconnection cable terminated with a lockable 8-pin DIN connector. It shall have a loopthrough connector to provide connection possibilities for subsequent call stations.

The design of the call station shall allow for both flush mounting in desktops and for tabletop use.

The call station shall provide facilities to make calls to all zones in a PA system (i.e. all-call). It shall not be possible to make calls to only a subset of zones in the system. The unit shall be provided with a green LED to give visible feedback on the active state of the microphone.

The call station shall have selectable gain, a selectable speech filter and a limiter for improved intelligibility in case the speaker moves in front of the microphone.

The call station shall provide a balanced line level output, to allow for positioning up to 450m away from the amplifier, using CAT-5 extension cables.

The priority level of the call station shall be determined by the matching amplifier, to which it is connected. In combination with the matching amplifier different pre- and post announcement chimes shall be available for selection.

The unit shall have an operating temperature range of –10 to +55(C. The unit shall comply with EN55103-1 and EN55103-2 for EMC emission and immunity.

The call station shall be a Plena model LBB1941/00, manufactured by Bosch Security Systems.

| 3122 475 21312 en | 03-40 | © 2003 Robert Bosch GmbH Data subject to change without notice. |
| --- | --- | --- |