### PLENA table-top microphone LBB1950/00

### Architects’ and Engineers’ Specifications

The table-top microphone shall have a metal base for stability, a flexible microphone stem and a uni-directional condenser microphone.

The table-top microphone shall be equipped with a 2m interconnection cable, terminated with a lockable 5-pin DIN connector, providing a balanced signal and priority contacts.

The design of the call station shall allow for both flush mounting in desk tops and for tabletop use.

The microphone shall be powered by the phantom power supply of the amplifier where it is connected to. It shall have a PTT (Press-To-Talk)-key, that switches on the microphone and also provides the priority contacts. It shall be possible to select the switching characteristic of the PTT-key internally between momentary (on as long as pressed) and latching (press to switch on, press again to switch off) behaviour.

A green LED shall indicate that the microphone is active, when the PTT-key is activated.

The unit shall be supplied with a separate 5-pin DIN to 3-pin XLR adapter, to facilitate connection to amplifiers with 3-pin XLR inputs, in case the priority contacts are not needed.

The unit shall have an operating temperature range of –10 to +55(C. The unit shall comply to EN55103-1 and EN55103-2 for EMC emission and immunity.

The call station shall be a Plena model LBB1950/10, manufactured by Bosch Security Systems.

| 3122 475 21513 en | 03-40 | © 2003 Robert Bosch GmbH Data subject to change without notice. |
| --- | --- | --- |