June 2009

| Americas Bosch Security Systems, Inc. 130 Perinton Parkway Fairport, New York, 14450, USA Phone: + 1 800 289 0096 Fax: +1 585 223 9180 security.sales@us.bosch.com www.boschsecurity.us | Europe, Middle East, Africa Bosch Security Systems B.V. P.O. Box 80002 5600 JB Eindhoven, The Netherlands Phone: + 31 40 2577 284 Fax: +31 40 2577 330 emea.securitysystems@bosch.com www.boschsecurity.com | Asia-Pacific Bosch Security Systems Pte Ltd 38C Jalan Pemimpin Singapore 577180 Phone: +65 6319 3450 Fax: +65 6319 3499 apr.securitysystems@bosch.com www.boschsecurity.com |
| --- | --- | --- |

Product Guide Specification

SECTION 28 23 16

VIDEO SURVEILLANCE MONITORING AND SUPERVISORY INTERFACES

BOSCH UML SERIES GENERAL PURPOSE COLOR LCD FLAT PANEL MONITORS

- – GENERAL

  - SUMMARY

    - Section Includes:

      - Video Surveillance Monitoring and Supervisory Interfaces.

    - Related Sections

      - Section [28 23 13 – Video Surveillance Control and Management Systems].

      - Section [28 23 23 – Video Surveillance Systems Infrastructure].

**********Specifier’s note: Include those standards referenced elsewhere in this SECTION.

  - REFERENCES

    - Complies with Canadian Standards Association (CSA).

    - European Norm:

      - Complies with EN Standards.

    - Federal Communications Commission (FCC) (www.fcc.gov):

      - FCC CFR 47 part 15 class A – Telecommunications – Radio Frequency Devices – Digital Device Emission.

    - Complies with International Electrotechnical Commission (IEC) standards.

    - Complies with International Committee on Electromagnetic Safety (ICES) 003 regulations.

    - International Organization for Standardization (ISO):

      - 9001 – Quality System.

    - Underwriters Laboratories, Inc. (UL) (www.ul.com):

      - UL 50 Enclosures for Electrical Equipment.

      - UL 2043 Fire Test for Heat and Visible Smoke Release for Discrete Products and their Accessories Installed in Air-Handling Spaces.

      - UL 60950-1 Information Technology Equipment - Safety.

  - DEFINITIONS

    - LCD: A Liquid Crystal Display is a thin, flat display device made up of any number of color or monochrome pixels arrayed in front of a light source or reflector.

    - Response Time: The minimum time necessary to change a pixel's color or brightness.

    - S-video: Separate video, also known as Y/C, is an analogue video signal that carries the video data as two separate signals: brightness and color.

    - Contrast Ratio: The ratio of the intensity of the brightest bright to the darkest dark.

  - SYSTEM DESCRIPTION

    - Video Surveillance Monitoring and Supervisory Interfaces:

      - General Purpose Color Flat Panel LCD Monitor.

    - Performance Requirements

      - Maximum contrast ratio of 600:1 to 1000:1.

      - Minimum response time of five to eight milliseconds.

      - Monitor must receive analog video signals, digital video signals, and computer video signals.

      - Must be able to mount the monitor to a wall or to a rack, or to place the monitor on a desktop with a stand.

      - The monitor must automatically adapt to the input resolution of the incoming video signal.

  - SUBMITTALS

    - Submit under provisions of Section [01 33 00].

    - Product Data:

      - Manufacturer’s data, user and installation manuals for all equipment and software programs including computer equipment and other equipment required for complete video management system.

    - Shop Drawings; include:

      - System device locations on architectural floor plans.

      - Full Schematic of system, including wiring information for all devices.

    - Closeout Submittals:

      - User manual.

      - Parts list.

      - System device locations on architectural floor plans.

      - Wiring and connection diagram.

      - Maintenance requirements.

  - QUALITY ASSURANCE

    - Manufacturer:

      - Minimum of [10] years experience in manufacture and design Video Surveillance Devices.

      - Manufacturer’s quality system: Registered to ISO 9001 Quality Standard.

    - Video Surveillance System:

      - Listed by [UL] [EN] [FCC] specifically for the required loads.  Provide evidence of compliance upon request.

    - Installer:

      - Minimum of [5] years experience installing Video Surveillance System.

  - DELIVERY, STORAGE AND HANDLING

    - Comply with requirements of Section [01 60 00].

    - Deliver materials in manufacture’s original, unopened, undamaged containers; and unharmed original identification labels.

    - Protect store materials from environmental and temperature conditions following manufacturer’s instructions.

    - Handle and operate products and systems according to manufacturer’s instructions.

    - Bosch provides off-the-shelf availability for our top selling products and same-day or 24-hour shipping.

  - WARRANTY

    - Provide manufacturer’s warranty covering [3] years for replacement and repair of defective equipment.

  - MAINTENANCE

    - Make ordering of new equipment for expansions, replacements, and spare parts available to dealers and end users.

    - Provide factory direct technical support from 8:00 a.m. to 8:00 p.m. via phone and e-mail.

- – PRODUCTS

  - MANUFACTURERS

    - Acceptable Manufacturer:

[Bosch Security Systems, Inc.

130 Perinton Parkway

Fairport, New York, 1450, USA

Phone: + 1 800 289 0096

Fax: + 1 585 223 9180

security.sales@us.bosch.com

www.boschsecurity.us]

[Bosch Security Systems B.V.

P.O. Box 80002

5600 JB Eindhoven, The Netherlands

Phone: + 31 40 2577 284

Fax: +31 40 2577 330

emea.securitysystems@bosch.com

www.boschsecurity.com]

[Bosch Security Systems Pte Ltd

38C Jalan Pemimpin

Singapore 577180

Phone: +65 6319 3450

Fax: +65 6319 3499

apr.securitysystems@bosch.com

www.boschsecurity.com]

    - Substitutions: [Not permitted.] [Under provisions of Division 1.]

      - [All proposed substitutions must be approved by the Architect or Engineer professional.]

      - [Proposed substitutions must provide a line-by-line compliance documentation.]

**********Specifier’s note: Select monitor based on project requirement. The Bosch UML Series of general purpose monitors contain three sizes (a 15-in., a 17-in., and a 19-in.); therefore you have a choice of monitor for each application.

  - BOSCH GENERAL PURPOSE COLOR LCD FLAT PANEL MONITOR [UML-151-90] [UML-171-90] [UML-191-90]

    - The flat panel LCD monitor shall have performance-enhancing features such as VGA inputs for DVR and PC applications, looping BNC output, Y/C (S-video) inputs, and compatibility with, at a minimum, these Bosch products:

      - Bosch Allegiant series switcher/controller.

      - Divar Easy, Divar MR, Divar XF, and DiBos digital video recorders.

      - Bosch IP network video solutions like the VIDOS video management system, and the Bosch Video Management System (BVMS).

    - The flat panel LCD monitor shall provide a front panel that allows the user to adjust image quality, brightness, size, position, and geometry for optimal viewing.

    - The flat panel LCD monitor shall provide a front panel control lockout feature so that only authorized users can adjust menu settings.

    - The flat panel LCD monitor shall avoid luminance degradation by:

      - Using long-life fluorescent backlights.

      - Each fluorescent backlight shall have a rated life of 50,000 hours.

    - The flat panel LCD monitor shall automatically adapt to the input resolution of the incoming video signal:

      - UML-151-90: shall adapt to a maximum resolution of 1024 x 768 pixels.

      - [UML-171-90] [UML-191-90]: shall adapt to a maximum resolution of 1280 x 1024 pixels.

    - The flat panel LCD monitor shall automatically adapt to fluctuating electricity loads.

    - Electrical:

      - [UML-151-90] [UML-171-90] [UML-191-90]:

        - Main supply input voltage: 120 VAC, 60 Hz or 230 VAC, 50 Hz.

        - Monitor Input Voltage/Power Requirements: 100–240 VAC.

        - Sync Format: PAL/NTSC.

        - LCD Panel: TFT LCD.

        - Rated Life: 50,000 hours.

      - UML-151-90:

        - Power Draw (typical): 25 W.

        - Screen Size (H x V): 304.1 x 228.1 mm (12.0 x 9.0 in.).

        - Viewable Picture Area: 15 in. (381 mm), measured diagonally.

        - Pixel Pitch (H x V): 0.297 x 0.297 mm (0.01 x 0.01 in.).

        - Resolution: 1024 x 768 pixels, 500 TV lines typical.

        - Aspect Ratio: 4:3.

        - Display Colors: 16.7 million colors.

        - Response Time: 8 milliseconds.

      - UML-171-90:

        - Power Draw (typical): 40 W.

        - Screen Size (H x V): 338.0 x 270.0 mm (13.3 x 10.6 in.).

        - Viewable Picture Area: 17 in. (432 mm), measured diagonally.

        - Pixel Pitch (H x V): 0.264 x 0.264 mm (0.01 x 0.01 in.).

        - Resolution: 1280 x 1024 pixels, 500 TV lines typical.

        - Aspect Ratio: 5:4.

        - Display Colors: 16.7 million colors.

        - Response Time: < 5 milliseconds.

      - UML-191-90:

        - Power Draw: 45 W.

        - Screen Size (H x V): 376.0 x 301.0 mm (14.8 x 11.9 in.).

        - Viewable Picture Area: 19 in. (483 mm), measured diagonally.

        - Pixel Pitch (H x V): 0.294 x 0.294 mm (0.01 x 0.01 in.).

        - Resolution: 1280 x 1024 pixels, 500 TV lines typical.

        - Aspect Ratio: 5:4.

        - Display Colors: 8-bit interface; 16.7 million colors.

        - Response Time: 5 milliseconds.

    - Mechanical:

      - [UML-151-90] [UML-171-90] [UML-191-90]:

        - Cabinet Material: ABS Plastic.

        - Finish: Black.

        - Mount: Wall mounting compatible with standard bracket, 100 mm (3.9 in.) centers, M4 thread.

      - UML-151-90:

        - Viewing Angle (Horizontal/Vertical): 160°/160°.

        - Weight, Monitor with Base: 3.7 kg (8.1 lb).

        - Weight, Monitor Only: 2.5 kg (5.6 lb).

        - Dimensions (W x H x D), Monitor with Base:

352 x 355 x 200 mm (13.86 x 14.0 x 7.9 in.).

        - Dimensions (W x H x D), Monitor Only:

352 x 292 x 58 mm (13.9 x 11.5 x 2.2 in.).

      - UML-171-90:

        - Viewing Angle (Horizontal/Vertical): 160°/160°.

        - Weight, Monitor with Base: 4.9 kg (10.8 lb).

        - Weight, Monitor Only: 3.8 kg (8.4 lb).

        - Dimensions (W x H x D), Monitor with Base:

382.4 x 390.5 x 200 mm (15.1 x 15.4 x 7.9 in.).

        - Dimensions (W x H x D), Monitor Only:

382.4 x 330.0 x 58.7 mm (15.1 x 13.0 x 2.3 in.).

      - UML-191-90:

        - Viewing Angle (Horizontal/Vertical): 160°/160°.

        - Weight, Monitor with Base: 5.2 kg (11.4 lb).

        - Weight, Monitor Only: 4.1 kg (9.0 lb).

        - Dimensions (W x H x D), Monitor with Base:

430 x 428 x 200 mm (16.9 x 16.9 x 7.9 in.).

        - Dimensions (W x H x D), Monitor Only:

420 x 374 x 60 mm (16.9 x 14.7 x 2.4 in.).

    - Environmental:

      - [UML-151-90] [UML-171-90] [UML-191-90]:

        - Operating Temperature: 0( to 40(C (32( to 104(F).

        - Storage Temperature: -20( to 60(C (-4( to 140(F).

        - Humidity: Maximum 90%, non-condensing.

  - ACCESSORIES

    - Mounts

      - Fixed Wall Mount, black Bosch UMM-LW-20B.

      - Swivel/Tilt Wall Mount, black Bosch UMM-LW-30B.

- – EXECUTION

  - EXAMINATION

    - Examine areas to receive devices and notify adverse conditions affecting installation or subsequent operation.

    - Do not begin installation until unacceptable conditions are corrected.

  - PREPARATION

    - Protect devices from damage during construction.

  - INSTALLATION

    - Install devices in accordance with manufacturer’s instruction at locations indicated on the floor drawings plans.

    - Perform installation with qualified service personnel.

    - Install devices in accordance with the National Electrical Code or applicable local codes.

    - Ensure selected location is secure and offers protection from accidental damage.

    - Location must provide reasonable temperature and humidity conditions, free from sources of electrical and electromagnetic interference.

  - FIELD QUALITY CONTROL

    - Test snugness of mounting screws of all installed equipment.

    - Test proper operation of all video system devices.

    - Determine and report all problems to the manufacturer’s customer service department.

  - ADJUSTING

    - Make proper adjustment to video system devices for correct operation in accordance with manufacturer’s instructions.

    - Make any adjustment of camera settings to comply with specific customer’s need.

  - DEMOSTRATION

    - Demonstrate at final inspection that video management system and devices functions properly.

END OF SECTION

# Text boxes

Specifier Notes:  This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format, based on MasterFormat 2004 and The Project Resource Manual—CSI Manual of Practice. The Manufacturer is responsible for technical accuracy.

The section must be carefully reviewed and edited by the Architect or Engineer to meet the requirements of the project and local building code.  Words and sentences within brackets [ ] are choices to include or exclude a particular item or statement.  Coordinate this section with other specification sections and the Drawings.  Delete all “Specifier Notes” after editing this section.