August 2015

| Americas Bosch Security Systems, Inc. 130 Perinton Parkway Fairport, New York, 14450, USA Phone: + 1 800 289 0096 Fax: +1 585 223 9180 security.sales@us.bosch.com www.boschsecurity.us | Europe, Middle East, Africa Bosch Security Systems B.V. P.O. Box 80002 5600 JB Eindhoven, The Netherlands Phone: + 31 40 2577 284 Fax: +31 40 2577 330 emea.securitysystems@bosch.com www.boschsecurity.com | Asia-Pacific Bosch Security Systems Pte Ltd 38C Jalan Pemimpin Singapore 577180 Phone: +65 6319 3450 Fax: +65 6319 3499 apr.securitysystems@bosch.com www.boschsecurity.com |
| --- | --- | --- |

Product Guide Specification

SECTION 28 23 19

DIGITAL VIDEO RECORDERS AND ANALOG RECORDING DEVICES

BOSCH DIVAR 3000 FAMILY

- – GENERAL

  - SUMMARY

    - Section Includes

      - Digital Video Recorders and Analog Recording Devices.

    - Related Sections

      - Section [28 23 16 – Video Surveillance Monitoring and Supervisory Interfaces].

      - Section [28 23 26 – Video Surveillance Remote Positioning Equipment].

      - Section [28 23 29 – Video Surveillance Remote Devices and Sensors].

  - REFERENCES

    - EMC Directive

      - 2004/108/EC

    - EMC Immunity

      - EN50130-4:2011

    - EMC Emission

      - EN55022:2010, +AC:2011 Class B conducted+radiated emission

      - EN61000-3-2:2006, +A1: 2009, +A2:2009 Mains harmonics

      - EN61000-3-3:2008 Voltage fluctuations

    - Environment

      - EN50130-5 Class 1

    - Low Voltage Directory

      - 2006/95/EC

    - Safety

      - EN 60950-1:2006, +A11:2009, +A1:2010, +A12:2011, +AC:2011

      - USA: UL 60950-1: 2nd edition 2011-12-19

      - CAN/CSA-C22.2 No.60950-1-07, 2nd edition 2011-12

    - FCC

      - CFR Title 47 Part 15:2011 class B

    - EMC Australia

      - C-Tick

  - SYSTEM DESCRIPTION

    - Digital Video Recorders and Analog Recording Devices.

      - Digital Video Recorder

    - Performance Requirements

      - The digital video recorder shall offer 960H high-resolution images via a HDMI output.

      - The digital video recorder shall offer 960H real time recording.

      - The digital video recorder shall allow simultaneous viewing of images from BNC and VGA outputs.

      - The digital video recorder shall support mobile devices (iOS and Android).

      - The digital video recorder shall provide remote alarm notification.

      - The digital video recorder shall offer a network function for remote viewing, playback and control.

      - The digital video recorder shall offer simultaneous monitoring, recording and playback.

      - The digital video recorder shall offer Web Client software.

  - SUBMITTALS

    - Submit under provisions of Section [01 33 00.]

    - Product Data:

      - Manufacturer’s data, operator and installation manuals software programs.

    - Shop Drawings; include

      - System device locations on architectural floor plans.

      - Full Schematic of system, including wiring information for all devices.

    - Closeout Submittals

      - User manual.

      - Parts list.

      - Connection diagram.

      - Installation CD.

      - Software license.

  - QUALITY ASSURANCE

    - Manufacturer:

      - Minimum of [10] years experience in manufacture and design of electronic security systems including sophisticated PC-based systems and digital products.

    - Manufacturer’s quality system: Registered to ISO 9001:2000 Quality Standard.

    - Installer:

      - Minimum of [5] years experience installing IP CCTV systems.

  - DELIVERY, STORAGE AND HANDLING

    - Comply with requirements of Section [01 60 00].

    - Deliver materials in manufacturer’s original, unopened, undamaged packaging; and unharmed original identification labels.

    - Protect store materials from environmental and temperature conditions following manufacturer’s instructions.

    - Handle and operate products and systems according to manufacturer’s instructions for installation, environmental, mechanical or electrical requirements and within thermal stress limits.

    - Ensure conformance with operating limitations according to applicable data sheet.

  - WARRANTY

    - Provide manufacturer’s warranty covering [3] years for CCTV products to repair and replace defective equipment.

    - Exchanges available for product failures.

  - MAINTENANCE

    - Make ordering of new equipment for expansions, replacements, and spare parts available to dealers and end users.

    - Provide factory direct technical support from 8:00 a.m. to 8:00 p.m. via phone or e-mail, or any time via Web.

      - Provide toll-free numbers to contact customer support.

    - Provide on-site training and on-line training via web.

- – PRODUCTS

  - MANUFACTURERS

    - Acceptable Manufacturer:

[Bosch Security Systems, Inc.

130 Perinton Parkway

Fairport, New York, 1450, USA

Phone: + 1 800 289 0096

Fax: + 1 585 223 9180

security.sales@us.bosch.com

www.boschsecurity.us]

[Bosch Security Systems B.V.

P.O. Box 80002

5600 JB Eindhoven, The Netherlands

Phone: + 31 40 2577 284

Fax: +31 40 2577 330

emea.securitysystems@bosch.com

www.boschsecurity.com]

Robert Bosch (SEA) Pte Ltd

11 Bishan Street 21

Singapore 573943

Phone: +65 6258 5511

Fax: +65 6571 2699

apr.securitysystems@bosch.com

www.boschsecurity.com

    - Substitutions: [Not permitted.] [Under provisions of Division 1.]

      - [All proposed substitutions must be approved by the Architect or Engineer professional.]

      - [Proposed substitutions must provide a line-by-line compliance documentation.]

  - BOSCH DIVAR 3000 FAMILY [DVR-3000-04A000] [DVR-3000-08A000] 
[DVR-3000-16A000] [DVR-3000-04A001] [DVR-3000-08A001] [DVR-3000-16A001] [DVR-3000-04A100] [DVR-3000-08A100] [DVR-3000-16A100] [DVR-3000-04A101] [DVR-3000-08A101] [DVR-3000-16A101] [DVR-3000-04A200] [DVR-3000-08A200] [DVR-3000-16A200] [DVR-3000-04A201] [DVR-3000-08A201] [DVR-3000-16A201]

    - General Description

      - The digital video recorder shall offer 960H high-resolution images via a HDMI output.

      - The digital video recorder shall offer 960H real time recording.

      - The digital video recorder shall allow simultaneous viewing of images from BNC and VGA outputs.

      - The digital video recorder shall support the use of a DVR smartphone app (iOS and Android) that allows live viewing and PTZ control.

      - The digital video recorder shall provide remote alarm notification.

      - The digital video recorder shall offer a network function for remote viewing, playback and control.

      - The digital video recorder shall offer simultaneous monitoring, recording and playback.

      - The digital video recorder shall offer models with 4, 8 or 16 auto-terminating BNC camera inputs.

      - The digital video recorder shall use H.264 video and G.711 audio compression technology.

      - The digital video recorder shall support bi-directional audio.

      - The digital video recorder shall be capable of recording multiple video and audio signals while simultaneously providing live multi-screen viewing and playback.

      - The digital video recorder shall offer comprehensive search and playback functions.

      - The digital video recorder shall allow viewing, playback and configuration via a remote Web management connection.

      - The digital video recorder shall come with software that allows a PC client to simultaneously display video from multiple recorders.

    - Recording

      - The digital video recorder shall simultaneously record 4, 8 or 16 channels using H.264 compression.

      - The digital video recorder shall record at up to 25 (PAL) / 30 (NTSC) images per second, per channel at 960H resolution.

      - The digital video recorder shall allow manual and automatic recording.

      - The digital video recorder shall allow automatic recording via a schedule or based on an alarm.

      - The digital video recorder shall provide a covert recording channel.

    - Alarms

      - The digital video recorder shall offer 16 switching (alarm) inputs and 3 alarm outputs.

      - The digital video recorder shall be capable of performing one of the following actions if an alarm is detected:

        - Send an e-mail notification and/or FTP push

        - Display an on-screen message

        - Sound a buzzer and/or show a warning light

    - Control

      - The digital video recorder shall offer the following methods to operate and program the unit via the on-screen display:

        - The supplied mouse

        - The front panel control keys

        - The supplied remote control

      - The digital video recorder shall provide auto-terminating video inputs, audio inputs/output, and alarm inputs/outputs on the rear panel of the device.

      - The digital video recorder shall offer three (3) video connectors (BNC/VGA/HDMI) to provide simultaneous output for monitor A for live display (with zoom) and playback.

      - The digital video recorder shall offer single BNC connector to provide output to monitor B (spot monitor) for live viewing.

      - The digital video recorder shall offer local archiving via a USB port, an optional built-in DVD writer or via a network video recording solution.

    - Dome Control

      - The digital video recorder shall offer an RS485 and an RS232 port interface for control of PTZ cameras.

      - The digital video recorder shall support the Bosch OSRD, Pelco P and Pelco D protocols.

    - Network Control

      - The digital video recorder shall contain a 10/100/1000Base-T Ethernet port for local or wide area network connection.

      - The digital video recorder shall support the use of PC software or a built-in web application via a network for live viewing, playback and configuration.

      - The digital video recorder shall include an authenticity check for locally or remotely generated archive files.

      - The digital video recorder shall offer bidirectional audio (audio input and output connected via device).

      - The digital video recorder shall offer an Archive Player for playback of secure video files and for video authentication.

    - Playback

      - The digital video recorder shall support simultaneous live viewing, playback or menu control via CVBS, VGA, and HDMI outputs (Monitor A).

      - The digital video recorder shall support live playback via CVBS output (Monitor B).

      - The digital video recorder shall support output to the PAL or NTSC video standard.

      - The digital video recorder shall support the following output resolutions:

        - CVBS (PAL): 704x576

        - CVBS (NTSC): 704x480

        - VGA: 1920x1080, 1280x1024, 1280x720, 1024x768

        - HDMI: 1920x1080, 1280x1024, 1280x720, 1024x768

        - 960H camera: 960x576 (PAL), 960x480 (NTSC)

        - 720H camera: 704x576 (PAL), 704x480 (NTSC)

      - The digital video recorder shall allow full-screen and multi-screen display capabilities in live and playback modes for monitors.

      - The digital video recorder shall offer the following playback modes:

        - Frame-by-frame

        - Slow play

        - Fast play

        - Reverse

    - PC requirements for Web Support

      - Operating system: Windows XP, Windows Vista or Windows 7

      - Web Browser: Safari, Chrome, Firefox (no playback supported), Internet Explorer 9 (including playback)

      - Processor: Intel Core Duo 2.0 GHz or comparable

      - RAM memory: 2048 MB

      - Free disk space: 10 MB

      - Graphics card: NVIDIA GeForce 8600 or better

      - Video Memory: 256 MB

      - Network interface: 10/100/1000-BaseT

    - Specifications

      - Electrical

        - External Power Adapter AC Input: 100–240 VAC; 50/60 Hz; 1.7 A

        - Power adapter DC output: 12 VDC; 5 A

        - DVR Power Output: 12 VDC; 5 A, 170 BTU/h

        - RTC Battery on Main PCB: Lithium CR2032, 3 VDC

      - Video

        - Video Standard:

          - PAL or NTSC (select via General Setup menu or auto detect on channel 1)

          - 960H resolution support

        - Playback:

          - 960H: 960x576 (PAL), 960x480 (NTSC)

          - 4CIF: 704x576 (PAL), 704x480 (NTSC)

          - 2CIF: 704x288 (PAL), 704x240 (NTSC)

          - CIF: 352x288 (PAL), 352x240 (NTSC)

          - QCIF: 176x144 (PAL), 176x120 (NTSC)

        - Compression: H.264

        - Inputs: 4, 8 or 16 composite video 1 Vpp, 75 ohm, CVBS (BNC)

        - Outputs:

          - 1 channel Mon. A: CVBS (BNC)

          - 1 channel Mon. A: HDMI

          - 1 channel Mon. A: VGA

          - 1 channel Mon. B: CVBS (BNC)

          - Support for simultaneous CVBS/VGA/HDMI output to Mon. A

      - Monitors

        - MON.A

          - Live, playback, menus

          - VGA: analog RGB max. 1920x1080, 60 Hz

          - HDMI: digital RGB max. 1920x1080, 165 MHz

          - CVBS: 1 Vpp, 75 ohm, BNC (NTSC/PAL)

        - MON.B

          - Live

          - CVBS: 1 Vpp, 75 ohm, BNC (NTSC/PAL)

        - Resolution (MON. A):

          - CVBS (PAL): 704x576

          - CVBS (NTSC): 704x480

          - VGA: 1920x1080, 1280x1024, 1280x720, 1024x768

          - HDMI: 1920x1080, 1280x1024, 1280x720, 1024x768

          - 960H camera: 960x576 (PAL), 960x480 (NTSC)

          - 720H camera: 704x576 (PAL), 704x480 (NTSC)

        - MON. B:

          - Live

          - CVBS: 1 Vpp, 75 ohm, BNC

        - Resolution (MON. B):

          - CVBS (PAL): 704x576

          - CVBS (NTSC): 704x480

      - Audio

        - Inputs: 4-ch RCA (for 4/8/16 channel), 200 to 3000 mV, 10 kOhm (RCA)

        - Output: Mono RCA, 200 to 3000 mV, 5 kOhm (RCA)

        - MIC Input: Mono talk input RCA, 200 to 3000 mV, 10 kOhm (RCA)

        - Compression: G.711A

        - Sample Rate: 8 kHz per channel

        - Bit Rate: 8-bit

      - Control

        - RS485:

          - PTZ control port

          - Output signals according to RS485,

          - Maximum signal voltage -5 to +5 V

        - RS232:

          - PTZ control port interface

          - Output signals according to EIA/TIA-232-F

          - Maximum input voltage ±10 V

        - Supported Protocols:

          - Pelco P and D (over RS-485)

          - Bosch OSRD (over RS-485 or RS-232)

      - Alarms

        - Inputs: 16 inputs configurable NO/NC, max. input voltage 5 VDC

        - Outputs: 3 relay outputs, configurable NO/NC

        - Relay Contact: Max. rated, 30 VDC, 2 A continuous or 125 VAC, 1 A (activated)

      - Connectors

        - Video Inputs: 4, 8 or 16 BNC

        - Monitor Outputs:

          - 1 VGA D-SUB

          - 1 HDMI

          - 2 channel BNC (CVBS)

        - Alarm Inputs: 16 screw terminal inputs, cable diameter 
AWG26‑16 (0.13–1.5 mm)

        - Alarm Outputs: 3 screw terminal outputs, cable diameter 
AWG26‑16 (0.13–1.5 mm)

        - Audio Inputs: 4 RCA

        - Audio Outputs: 1 RCA

        - Audio bidirectional (MIC): 1 RCA for talk input or output

        - Ethernet: RJ45, 10/100/1000Base-T according to IEEE802.3

        - RS485: Screw terminal output

        - RS232: DB9 male, 9-pin D-type

        - USB 2.0: One front and one rear USB connector for mouse or USB memory device

        - +12 VDC: External power input

      - Video Recording

        - Recording

          - Speed:

            - Max. 30 IPS per channel (NTSC), configurable

            - Max. 25 IPS per channel (PAL), configurable

          - Mode: Manual, motion detection, scheduled, alarm

        - Network Control

          - View Alarm: External, motion detection, system alarms and video loss

          - Audio: Bidirectional (audio input and output connected via device)

          - PC Software: Bosch Video Client

        - Playback:

          - Multi-channel: Simultaneous 1/4/9/16 channels

          - Mode:

            - Frame-by-frame

            - Slow play

            - Fast play

            - Reverse

          - Search

            - Time

            - Channel

            - Type

            - Smart

          - Network: Bosch Video Client or Web Client software

        - Alarm Handling

          - Motion Detection: Detection zones: 396 (PAL) / 330 (NTSC)

          - Video Loss: External alarm or screen prompt

        - Storage

          - Internal:

            - 2 SATA HDD or 1 HDD + 1 DVD (R/RW)

            - Maximum capacity per HDD: 4TB

            - Maximum supported speed per HDD: 6 Gb/s

        - Exporting

          - [DVD: Built-in DVD+R/RW writer]

          - USB: Flash memory or external HDD (FAT32)

          - Network: Bosch Video Client or Web Client software

      - Mechanical

        - Dimensions (WxDxH): 375 x 290 x 50 mm (14.8 x 11.4 x 2.0 in) excluding cabling and feet (5 mm)

        - Weight: 2.5 kg (5.51 lb) approx. excluding HDD(s) and DVD writer

      - Environmental

        - Operating Temperature: (including HDDs and DVD writer):
+0°C to +40°C (+32°F to +104°F)

        - Storage Temperature (including HDDs and DVD writer): 
-40°C to +70°C (-40°F to +158°F)

        - Operating Humidity: <93% non-condensing

        - Storage Humidity: <95% non-condensing

  - ACCESSORIES

    - DVR-XS050-A Storage Expansion Kit: 500 GB

    - DVR-XS100-A Storage Expansion Kit: 1 TB

    - DVR-XS200-A Storage Expansion Kit: 2 TB

    - DVR-XS300-A Storage Expansion Kit: 3 TB

    - DVR-XS400-A Storage Expansion Kit: 4 TB

    - DVR-XS-DVD DVD Writer Expansion Kit

- EXECUTION

- EXAMINATION

- Examine areas to receive devices and notify adverse conditions affecting installation or subsequent operation.

- Do not begin installation until unacceptable conditions are corrected.

- Non-compliance with security instructions may result in loss of data.

- Ensure environmental, mechanical and electrical requirements are met.

- PREPARATION

- Protect devices from damage during construction.

- INSTALLATION

    - Install devices in accordance with manufacturer's instruction at locations indicated on the floor drawings plans.

    - Perform installation with qualified service personnel.

    - Install devices in accordance with the National Electrical Code or applicable local codes.

    - Ensure selected location is secure and offers protection from accidental damage.

    - Location must provide reasonable temperature and humidity conditions, free from sources of electrical and electromagnetic interference.

- FIELD QUALITY CONTROL

- Test proper operation of all video system devices.

      - Communication between recorder and cameras.

      - Independent operation of alarms, and cameras.

- Test proper operation of software programs.

- Determine and report all problems to the manufacturer's customer service department.

- Determine and report all problems to the manufacturer’s customer service department.

- ADJUSTING

- Make proper adjustment to video system devices for correct operation in accordance with manufacturer’s instructions.

- Make any adjustment of camera settings to comply with specific customer's need.

- DEMONSTRATION

- Demonstrate at final inspection that playback of video and storage functions operate properly.

END OF SECTION

# Text boxes

Specifier Notes:  This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format, based on MasterFormat 2004 and The Project Resource Manual—CSI Manual of Practice. The Manufacturer is responsible for technical accuracy.

The section must be carefully reviewed and edited by the Architect or Engineer to meet the requirements of the project and local building code.  Words and sentences within brackets [ ] are choices to include or exclude a particular item or statement.  Coordinate this section with other specification sections and the Drawings.  Delete all “Specifier Notes” after editing this section.